## Slide 1
M3
Mini Mobile Marker
(Coaxial System Signal Leakage Pressure Testing)
Confidential Information

## Slide 2
Confidential
M3 (Mini Mobile Marker)
M3
Pressure Test
ComSonics M3 Pressure testing:
Exposes small defects in the cable shielding
Allows technician to detect leakage without entering customer premise
Allows leakage isolation on SDUs, MDU floors or individual apartments
Supports maximum shielding integrity at the drop and premise
Planned Release: Q2 2015
QAM
Shadow
QAM
Sniffer
TV
TV
TV
+60 dBmV
Marker signal
Uses Existing Equipment

## Slide 3: M3 – Application
Single Family Dwelling, Lots of Toys
An in-line pad inserted at the M3 output lowers the input level to the cable segment being tested.

## Slide 4: M3 – Shielding Integrity (SI) Determination
SI = M3 output level – pad value – splitter Loss – shadow pick-up capability (in Marker 4 mode) – free-space loss
Assume measurements are made:
With M3 output of +60 dBmV
With pad values as shown in table below
5 ‘ from the cabling (loss = 32 dB @ 612 MHz)
With cable from a two-way splitter (3.5 dB loss)
With Shadow max Readout = 1999 µV/m, and
With Shadow min readout = 1 µV/m.
Pad Value | SI Min | SI Max
0 | 40 dB | 106 dB
20 | 20 | 86
40 | 0 | 66

## Slide 5
Confidential
M3 (Mini Mobile Marker)
M3
Pressure Test
M3 Mini Mobile Marker Features
Generates a unique MID4 marker at +60 dBmV
Battery lasts for 8 hours on a single recharge
Has a fail-safe locking power switch
Provides radiated emission integrity greater than 120 dB
MID4 improves the QAM Shadow’s dynamic range to 66 dB
Planned Release: Q2 2015
QAM
Shadow
QAM
Sniffer
TV
TV
TV
+60 dBmV
Marker signal
Uses Existing Equipment